## Slide 1
Chapter 3
Introduction to Physical Layer

## Slide 2
Figure 3.1 Communication at the physical layer

## Slide 3
3.1.1 ANALOG AND DIGITAL DATA
Data can be analog or digital. The term analog data refers to information that is continuous; digital data refers to information that has discrete states. Analog data take on continuous values. Digital data take on discrete values.

## Slide 4
Note
Data can be analog or digital. Analog data are continuous and take continuous values.
Digital data have discrete states and take discrete values.

## Slide 5
Signals can be analog or digital. Analog signals can have an infinite number of values in a range; digital signals can have only a limited number of values.
Note
3.1.2 ANALOG AND DIGITAL SIGNALS

## Slide 6
Figure 3.3 Comparison of analog and digital signals

## Slide 7
3.1.3 PERIODIC & NONPERIODIC
Periodic signal
completes a pattern, and
repeats that pattern.
The completion of one full pattern is called a cycle.
Nonperiodic (aperiodic) signal
changes without exhibiting a pattern

## Slide 8
In data communications, we commonly use periodic analog signals and nonperiodic digital signals.
Note

## Slide 9
3.2 PERIODIC ANALOG SIGNALS
Periodic analog signals can be classified as simple or composite. A simple periodic analog signal, a sine wave, cannot be decomposed into simpler signals. A composite
periodic analog signal is composed of multiple sine waves.
Sine Wave Wavelength Time and Frequency Domain Composite Signals
Bandwidth
Topics discussed in this section:

## Slide 10
Figure 3.2 A sine wave

## Slide 11
Peak amplitude - absolute value of the signal highest intensity, proportional to the energy it carries
Frequency - the number of cycles in 1 s.
Phase - position of the waveform relative to time 0.
Peak Amplitude, Frequency and Phase

## Slide 12
Figure 3.4 Two signals with the same phase and frequency, but different amplitudes

## Slide 13
The power in U.S. home can be represented by a sine wave with a peak amplitude of 155 to 170 V.
However, voltage of the power in U.S. homes is 110 to 120 V.
The signal is squared and then the average amplitude is calculated. The peak value is equal to 2½ × rms value.
Example 3.1

## Slide 14
The voltage of a battery is a constant; this constant value can be considered a sine wave (as we will see later).
For example, the peak value of an AA battery is normally 1.5 V.
Example 3.2

## Slide 15
Frequency and period are the inverse of each other.

## Slide 16
Figure 3.5 Two signals with the same amplitude and phase, but different frequencies

## Slide 17
Table 3.1 Units of period and frequency

## Slide 18
The power we use at home has a frequency of 60 Hz. The period of this sine wave can be determined as follows:
Example 3.3

## Slide 19
Express a period of 100 ms in microseconds.
Example 3.4
Solution
From Table 3.1 we find the equivalents of 1 ms (1 ms is 10−3 s) and 1 s (1 s is 106 μs). We make the following substitutions:.

## Slide 20
The period of a signal is 100 ms. What is its frequency in kilohertz?
Example 3.5
Solution
First we change 100 ms to seconds, and then we calculate the frequency from the period (1 Hz = 10−3 kHz).

## Slide 21
Frequency is the rate of change with respect to time. Change in a short span of time
means high frequency. Change over a long span of time means low frequency.
Note

## Slide 22
If a signal does not change at all, its frequency is zero.
If a signal changes instantaneously, its frequency is infinite.
Note

## Slide 23
Phase describes the position of the waveform relative to time 0.
Note

## Slide 24
Figure 3.5 Three sine waves with the same amplitude and frequency, but different phases

## Slide 25
A sine wave is offset 1/6 cycle with respect to time 0. What is its phase in degrees and radians?
Example 3.6
Solution
We know that 1 complete cycle is 360°. Therefore, 1/6 cycle is

## Slide 26
Figure 3.7 Wavelength and period

## Slide 27
Figure 3.8 The time-domain and frequency-domain plots of a sine wave

## Slide 28
A complete sine wave in the time domain can be represented by one single spike in the frequency domain.
Note

## Slide 29
The frequency domain is more compact and useful when we are dealing with more than one sine wave.
For example, Figure 3.9 shows three sine waves, each with different amplitude and frequency.
All can be represented by three spikes in the frequency domain.
Example 3.7

## Slide 30
Figure 3.9 The time domain and frequency domain of three sine waves

## Slide 31
A single-frequency sine wave is not useful in data communications;
we need to send a composite signal, a signal made of many simple sine waves.
Note

## Slide 32
According to Fourier analysis, any composite signal is a combination of
simple sine waves with different frequencies, amplitudes, and phases.
Fourier analysis is discussed in Appendix E.
Note

## Slide 33
Periodic composite signal is periodic - series of signals with discrete frequencies;
Nonperiodic composite signal - a combination of sine waves with continuous frequencies.
Note

## Slide 34
Figure 3.9 shows a periodic composite signal with frequency f. This type of signal is not typical of those found in data communications. We can consider it to be three alarm systems, each with a different frequency. The analysis of this signal can give us a good understanding of how to decompose signals.
Example 3.8

## Slide 35
Figure 3.10 A composite periodic signal

## Slide 36
Figure 3.11 Decomposition of a composite periodic signal in the time and frequency domains

## Slide 37
Figure 3.11 shows a nonperiodic composite signal. It can be the signal created by a microphone or a telephone set when a word or two is pronounced. In this case, the composite signal cannot be periodic, because that implies that we are repeating the same word or words with exactly the same tone.
Example 3.9

## Slide 38
Figure 3.12 The time and frequency domains of a nonperiodic signal

## Slide 39
The range of frequencies contained in a composite signal is its bandwidth.
The bandwidth of a composite signal is the difference between the highest and the lowest frequencies contained in that signal.
Bandwidth

## Slide 40
Figure 3.13 The bandwidth of periodic and nonperiodic composite signals

## Slide 41
If a periodic signal is decomposed into five sine waves with frequencies of 100, 300, 500, 700, and 900 Hz, what is its bandwidth? Draw the spectrum, assuming all components have a maximum amplitude of 10 V.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.10
The spectrum has only five spikes, at 100, 300, 500, 700, and 900 Hz (see Figure 3.13).

## Slide 42
Figure 3.14 The bandwidth for Example 3.10

## Slide 43
A periodic signal has a bandwidth of 20 Hz. The highest frequency is 60 Hz. What is the lowest frequency? Draw the spectrum if the signal contains all frequencies of the same amplitude.
Solution
Let fh be the highest frequency, fl the lowest frequency, and B the bandwidth. Then
Example 3.11
The spectrum contains all integer frequencies. We show this by a series of spikes (see Figure 3.15).

## Slide 44
Figure 3.15 The bandwidth for Example 3.11

## Slide 45
A nonperiodic composite signal has a bandwidth of 200 kHz, with a middle frequency of 140 kHz and peak amplitude of 20 V. The two extreme frequencies have an amplitude of 0. Draw the frequency domain of the signal.
Solution
The lowest frequency must be at 40 kHz and the highest at 240 kHz. Figure 3.15 shows the frequency domain and the bandwidth.
Example 3.12

## Slide 46
Figure 3.16 The bandwidth for Example 3.12

## Slide 47
An example of a nonperiodic composite signal is the signal propagated by an AM radio station. In the United States, each AM radio station is assigned a 10-kHz bandwidth. The total bandwidth dedicated to AM radio ranges from 530 to 1700 kHz. We will show the rationale behind this 10-kHz bandwidth in Chapter 5.
Example 3.13

## Slide 48
Another example of a nonperiodic composite signal is the signal propagated by an FM radio station. In the United States, each FM radio station is assigned a 200-kHz bandwidth. The total bandwidth dedicated to FM radio ranges from 88 to 108 MHz. We will show the rationale behind this 200-kHz bandwidth in Chapter 5.
Example 3.14

## Slide 49
Another example of a nonperiodic composite signal is the signal received by an old-fashioned analog black-and-white TV. A TV screen is made up of pixels. If we assume a resolution of 525 × 700, we have 367,500 pixels per screen. If we scan the screen 30 times per second, this is 367,500 × 30 = 11,025,000 pixels per second. The worst-case scenario is alternating black and white pixels. We can send 2 pixels per cycle. Therefore, we need 11,025,000 / 2 = 5,512,500 cycles per second, or Hz. The bandwidth needed is 5.5125 MHz.
Example 3.15

## Slide 50
3.3 DIGITAL SIGNALS
In addition to being represented by an analog signal, information can also be represented by a digital signal. For example, a 1 can be encoded as a positive voltage and a 0 as zero voltage. A digital signal can have more than two levels. In this case, we can send more than 1 bit for each level.
Bit Rate Bit Length Digital Signal as a Composite Analog Signal
Application Layer
Topics discussed in this section:

## Slide 51
Figure 3.17 Two digital signals: one with two signal levels and the other with four signal levels

## Slide 52
Bit Rate: the number of bits sent in 1s, expressed in bits per second (bps).
Comparable to frequency of periodic analog signal.
Bit length: the distance one bit occupies on the transmission medium.

## Slide 53
A digital signal has eight levels. How many bits are needed per level? We calculate the number of bits from the formula
Example 3.16
Each signal level is represented by 3 bits.

## Slide 54
A digital signal has nine levels. How many bits are needed per level? We calculate the number of bits by using the formula. Each signal level is represented by 3.17 bits. However, this answer is not realistic. The number of bits sent per level needs to be an integer as well as a power of 2. For this example, 4 bits can represent one level.
Example 3.17

## Slide 55
Assume we need to download text documents at the rate of 100 pages per minute. What is the required bit rate of the channel?
Solution
A page is an average of 24 lines with 80 characters in each line. If we assume that one character requires 8 bits, the bit rate is
Example 3.18

## Slide 56
A digitized voice channel, as we will see in Chapter 4, is made by digitizing a 4-kHz bandwidth analog voice signal. We need to sample the signal at twice the highest frequency (two samples per hertz). We assume that each sample requires 8 bits. What is the required bit rate?
Solution
The bit rate can be calculated as
Example 3.19

## Slide 57
What is the bit rate for high-definition TV (HDTV)?
Solution
HDTV uses digital signals to broadcast high quality video signals. The HDTV screen is normally a ratio of 16 : 9. There are 1920 by 1080 pixels per screen, and the screen is renewed 30 times per second. Twenty-four bits represents one color pixel.
Example 3.20
The TV stations reduce this rate to 20 to 40 Mbps through compression.

## Slide 58
Digital Signal as a Composite Analog Signal

## Slide 59
Figure 3.18 The time and frequency domains of periodic and nonperiodic digital signals

## Slide 60: Transmission of Digital Signals
Baseband Transmission
(low-pass channel)
Sending a digital signal over a channel without changing
the digital signal to an analog signal

## Slide 61
A digital signal is a composite analog signal with an infinite bandwidth.
It starts from zero frequency.
Note

## Slide 62
Figure 3.19 Baseband transmission
Baseband transmission requires a low-pass channel.
Low-pass channel allows a bandwidth starting from zero.
Ideally low-pass channel with infinite bandwidth is required.
Sending a digital signal over a channel without changing
the digital signal to an analog signal.

## Slide 63
Figure 3.20 Bandwidths of two low-pass channels

## Slide 64
Figure 3.21 Baseband transmission using a dedicated medium
If f1 is very close to zero and f2 is very high, the vertical and horizontal components of the digital signal is affected in very small scale.

## Slide 65
Baseband transmission of a digital signal that preserves the shape of the digital signal is possible only if we have a low-pass channel with an infinite or very wide bandwidth.
Note

## Slide 66
An example of a dedicated channel where the entire bandwidth of the medium is used as one single channel is a LAN. Almost every wired LAN today uses a dedicated channel for two stations communicating with each other. In a bus topology LAN with multipoint connections, only two stations can communicate with each other at each moment in time (timesharing); the other stations need to refrain from sending data. In a star topology LAN, the entire channel between each station and the hub is used for communication between these two entities. We study LANs in Chapter 14.
Example 3.21

## Slide 67
Figure 3.21 Rough approximation of a digital signal using the first harmonic for worst case

## Slide 68
Figure 3.22 Simulating a digital signal with first three harmonics
https://www.desmos.com/calculator/5yp953jhxu

## Slide 69
In baseband transmission, the required bandwidth is proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.
Note
In baseband transmission, the required bandwidth is proportional to the bit rate;
if we need to send bits faster, we need more bandwidth.

## Slide 70
Table 3.2 Bandwidth requirements

## Slide 71
What is the required bandwidth of a low-pass channel if we need to send 1 Mbps by using baseband transmission?
Solution
The answer depends on the accuracy desired.
a. The minimum bandwidth, is B = bit rate /2, or 500 kHz.
b. A better solution is to use the first and the third harmonics with B = 3 × 500 kHz = 1.5 MHz.
c. Still a better solution is to use the first, third, and fifth harmonics with B = 5 × 500 kHz = 2.5 MHz.
Example 3.22

## Slide 72
We have a low-pass channel with bandwidth 100 kHz. What is the maximum bit rate of this channel?
Solution
The maximum bit rate can be achieved if we use the first harmonic. The bit rate is 2 times the available bandwidth, or 200 kbps.
Example 3.22

## Slide 73
Broadband Transmission
(Using Modulation)
changing the digital signal to an analog signal for transmission.

## Slide 74
Figure 3.24 Bandwidth of a bandpass channel

## Slide 75
If the available channel is a bandpass channel, we cannot send the digital signal directly to the channel; we need to convert the digital signal to an analog signal before transmission.
Note

## Slide 76
Figure 3.25 Modulation of a digital signal for transmission on a bandpass channel

## Slide 77
An example of broadband transmission using modulation is the sending of computer data through a telephone subscriber line, the line connecting a resident to the central telephone office. These lines are designed to carry voice with a limited bandwidth. The channel is considered a bandpass channel. We convert the digital signal from the computer to an analog signal, and send the analog signal. We can install two converters to change the digital signal to analog and vice versa at the receiving end. The converter, in this case, is called a modem which we discuss in detail in Chapter 5.
Example 3.24

## Slide 78
A second example is the digital cellular telephone. For better reception, digital cellular phones convert the analog voice signal to a digital signal (see Chapter 16). Although the bandwidth allocated to a company providing digital cellular phone service is very wide, we still cannot send the digital signal without conversion. The reason is that we only have a bandpass channel available between caller and callee. We need to convert the digitized voice to a composite analog signal before sending.
Example 3.25

## Slide 79
3-4 TRANSMISSION IMPAIRMENT
Signals travel through transmission media, which are not perfect. The imperfection causes signal impairment. This means that the signal at the beginning of the medium is not the same as the signal at the end of the medium. What is sent is not what is received. Three causes of impairment are attenuation, distortion, and noise.
Attenuation Distortion Noise
Topics discussed in this section:

## Slide 80
Figure 3.26 Causes of impairment

## Slide 81
Figure 3.27 Attenuation

## Slide 82
Suppose a signal travels through a transmission medium and its power is reduced to one-half. This means that P2 is (1/2)P1. In this case, the attenuation (loss of power) can be calculated as
Example 3.26
A loss of 3 dB (–3 dB) is equivalent to losing one-half the power.

## Slide 83
A signal travels through an amplifier, and its power is increased 10 times. This means that P2 = 10P1 . In this case, the amplification (gain of power) can be calculated as
Example 3.27

## Slide 84
One reason that engineers use the decibel to measure the changes in the strength of a signal is that decibel numbers can be added (or subtracted) when we are measuring several points (cascading) instead of just two. In Figure 3.27 a signal travels from point 1 to point 4. In this case, the decibel value can be calculated as
Example 3.28

## Slide 85
Figure 3.28 Decibels for Example 3.28

## Slide 86
Sometimes the decibel is used to measure signal power in milliwatts. In this case, it is referred to as dBm and is calculated as dBm = 10 log10 Pm , where Pm is the power in milliwatts. Calculate the power of a signal with dBm = −30.
Solution
We can calculate the power in the signal as
Example 3.29

## Slide 87
The loss in a cable is usually defined in decibels per kilometer (dB/km). If the signal at the beginning of a cable with −0.3 dB/km has a power of 2 mW, what is the power of the signal at 5 km?
Solution
The loss in the cable in decibels is 5 × (−0.3) = −1.5 dB. We can calculate the power as
Example 3.30

## Slide 88
Distortion
Distortion means that the signal changes its form or shape

## Slide 89
Figure 3.29 Distortion

## Slide 90
Figure 3.30 Noise

## Slide 91
The power of a signal is 10 mW and the power of the noise is 1 μW; what are the values of SNR and SNRdB ?
Solution
The values of SNR and SNRdB can be calculated as follows:
Example 3.31

## Slide 92
The values of SNR and SNRdB for a noiseless channel are
Example 3.32
We can never achieve this ratio in real life; it is an ideal.

## Slide 93
Figure 3.31 Two cases of SNR: a high SNR and a low SNR

## Slide 94
3-5 DATA RATE LIMITS
A very important consideration in data communications is how fast we can send data, in bits per second, over a channel. Data rate depends on three factors:
1. The bandwidth available
2. The level of the signals we use
3. The quality of the channel (the level of noise)
Noiseless Channel: Nyquist Bit Rate Noisy Channel: Shannon Capacity Using Both Limits
Topics discussed in this section:

## Slide 95
Noiseless Channel: Nyquist Bit Rate
BitRate = 2 x bandwidth x log2L
formula

## Slide 96
Increasing the levels of a signal may reduce the reliability of the system.
Note

## Slide 97
Consider a noiseless channel with a bandwidth of 3000 Hz transmitting a signal with two signal levels. The maximum bit rate can be calculated as
Example 3.34

## Slide 98
Consider the same noiseless channel transmitting a signal with four signal levels (for each level, we send 2 bits). The maximum bit rate can be calculated as
Example 3.35

## Slide 99
We need to send 265 kbps over a noiseless channel with a bandwidth of 20 kHz. How many signal levels do we need?
Solution
We can use the Nyquist formula as shown:
Example 3.36
Since this result is not a power of 2, we need to either increase the number of levels or reduce the bit rate. If we have 128 levels, the bit rate is 280 kbps. If we have 64 levels, the bit rate is 240 kbps.

## Slide 100
Noisy Channel: Shannon Capacity
Capacity = bandwidth x log2(1 + SNR)
formula

## Slide 101
Consider an extremely noisy channel in which the value of the signal-to-noise ratio is almost zero. In other words, the noise is so strong that the signal is faint. For this channel the capacity C is calculated as
Example 3.37
This means that the capacity of this channel is zero regardless of the bandwidth. In other words, we cannot receive any data through this channel.

## Slide 102
We can calculate the theoretical highest bit rate of a regular telephone line. A telephone line normally has a bandwidth of 3000. The signal-to-noise ratio is usually 3162. For this channel the capacity is calculated as
Example 3.38
This means that the highest bit rate for a telephone line is 34.860 kbps. If we want to send data faster than this, we can either increase the bandwidth of the line or improve the signal-to-noise ratio.

## Slide 103
The signal-to-noise ratio is often given in decibels. Assume that SNRdB = 36 and the channel bandwidth is 2 MHz. The theoretical channel capacity can be calculated as
Example 3.39

## Slide 104
For practical purposes, when the SNR is very high, we can assume that SNR + 1 is almost the same as SNR. In these cases, the theoretical channel capacity can be simplified to
Example 3.40
For example, we can calculate the theoretical capacity of the previous example as

## Slide 105
We have a channel with a 1-MHz bandwidth. The SNR for this channel is 63. What are the appropriate bit rate and signal level?
Solution
First, we use the Shannon formula to find the upper limit.
Example 3.41

## Slide 106
The Shannon formula gives us 6 Mbps, the upper limit. For better performance we choose something lower, 4 Mbps, for example. Then we use the Nyquist formula to find the number of signal levels.
Example 3.41 (continued)

## Slide 107
The Shannon capacity gives us the upper limit; the Nyquist formula tells us how many signal levels we need.
Note

## Slide 108
3-6 PERFORMANCE
One important issue in networking is the performance of the network—how good is it? We discuss quality of service, an overall measurement of network performance, in greater detail in Chapter 24. In this section, we introduce terms that we need for future chapters.
Bandwidth Throughput Latency (Delay)
Bandwidth-Delay Product
Topics discussed in this section:

## Slide 109
In networking, we use the term bandwidth in two contexts.
❏The first, bandwidth in hertz, refers to the range of frequencies in a composite signal or the range of frequencies that a channel can pass.
❏The second, bandwidth in bits per second, refers to the speed of bit transmission in a channel or link.
Note
Performance: Bandwidth

## Slide 110
The bandwidth of a subscriber line is 4 kHz for voice or data. The bandwidth of this line for data transmission
can be up to 56,000 bps using a sophisticated modem to change the digital signal to analog.
Example 3.42

## Slide 111
If the telephone company improves the quality of the line and increases the bandwidth to 8 kHz, we can send 112,000 bps by using the same technology as mentioned in Example 3.42.
Example 3.43

## Slide 112
A network with bandwidth of 10 Mbps can pass only an average of 12,000 frames per minute with each frame carrying an average of 10,000 bits. What is the throughput of this network?
Solution
We can calculate the throughput as
Example 3.44
The throughput is almost one-fifth of the bandwidth in this case.

## Slide 113
What is the propagation time if the distance between the two points is 12,000 km? Assume the propagation speed to be 2.4 × 108 m/s in cable.
Solution
We can calculate the propagation time as
Example 3.45
The example shows that a bit can go over the Atlantic Ocean in only 50 ms if there is a direct cable between the source and the destination.

## Slide 114
What are the propagation time and the transmission time for a 2.5-kbyte message (an e-mail) if the bandwidth of the network is 1 Gbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission time as shown on the next slide:
Example 3.46

## Slide 115
Note that in this case, because the message is short and the bandwidth is high, the dominant factor is the propagation time, not the transmission time. The transmission time can be ignored.
Example 3.46 (continued)

## Slide 116
What are the propagation time and the transmission time for a 5-Mbyte message (an image) if the bandwidth of the network is 1 Mbps? Assume that the distance between the sender and the receiver is 12,000 km and that light travels at 2.4 × 108 m/s.
Solution
We can calculate the propagation and transmission times as shown on the next slide.
Example 3.47

## Slide 117
Note that in this case, because the message is very long and the bandwidth is not very high, the dominant factor is the transmission time, not the propagation time. The propagation time can be ignored.
Example 3.47 (continued)

## Slide 118
Figure 3.32 Filling the link with bits for case 1

## Slide 119
We can think about the link between two points as a pipe. The cross section of the pipe represents the bandwidth, and the length of the pipe represents the delay. We can say the volume of the pipe defines the bandwidth-delay product, as shown in Figure 3.33.
Example 3.48

## Slide 120
Figure 3.33 Filling the link with bits in case 2

## Slide 121
The bandwidth-delay product defines the number of bits that can fill the link.
Note

## Slide 122
Figure 3.34 Concept of bandwidth-delay product