## Slide 1: Chapter 10 Error Detection and Correction

## Slide 2
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Note

## Slide 3
10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Types of Errors Redundancy Detection Versus Correction Forward Error Correction Versus Retransmission Coding
Modular Arithmetic
Topics discussed in this section:

## Slide 4: Introduction
Error transmissions are caused by Interference
Types of errors
  Single-bit error
    Only 1 bit of a given data unit is changed from 1 to 0 or from 0 to 1.
  Burst error
    2 or more bits in the data unit changed from 1 to 0 or from 0 to 1.
Redundancy
  The central concept in detecting or correcting error is redundancy. To be able to detect or correct errors, we need to send some extra bits with our data.

## Slide 5
Figure 10.1 Single-bit and burst error

## Slide 6
To detect or correct errors, we need to send extra (redundant) bits with data.
Note

## Slide 7: Detection versus Correction
The correction of errors is more difficult than the detection.
Error detection
  Looking only to see if any error has occurred
  The answer is a simple yes or no.
Error correction
  Forward error correction
    The process in which the receiver tries to guess the message by using redundant bits.
  Retransmission
    The receiver detects the occurrence of an error and asks the sender to resend the message.

## Slide 8: Coding
Redundancy is achieved through various coding schemes.
It creates a relationship between the redundant bits and the actual data bits.
Two consideration
  The ratio of redundant bits to data bits.
  the robustness of the process.
Two broad categories:
  Block coding and
  Convolution coding.

## Slide 9
In modulo-N arithmetic, we use only the integers in the range 0 to N −1, inclusive.
Note

## Slide 10
Figure 10.4 XORing of two single bits or two words

## Slide 11
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
Error Detection Error Correction Hamming Distance
Minimum Hamming Distance
Topics discussed in this section:

## Slide 12
Figure 10.2 Process of error detection in block coding

## Slide 13: Error Detection
To detect the change in the original codeword
  The receiver has (or can find) a list of valid codewords.
  The original codeword has changed to an invalid one.

## Slide 14
Figure 10.5 Datawords and codewords in block coding

## Slide 15
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Assume the sender encodes the dataword 01 as 011 and
sends it to the receiver. Consider the following cases:
1. The receiver receives 011. It is a valid codeword. The receiver extracts the dataword 01 from it.
Example 10.1

## Slide 16
2. The codeword is corrupted during transmission, and 111 is received. This is not a valid codeword and is discarded.
3. The codeword is corrupted during transmission, and 000 is received. This is a valid codeword. The receiver incorrectly extracts the dataword 00. Two corrupted bits have made the error undetectable.
Example 10.2 (continued)

## Slide 17
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note

## Slide 18
Let us add more redundant bits to Example 10.2 to see if the receiver can correct an error without knowing what was actually sent. We add 3 redundant bits to the 2-bit dataword to make 5-bit codewords. Table 10.2 shows the datawords and codewords. Assume the dataword is 01. The sender creates the codeword 01011. The codeword is corrupted during transmission, and 01001 is received. First, the receiver finds that the received codeword is not in the table. This means an error has occurred. The receiver, assuming that there is only 1 bit corrupted, uses the following strategy to guess the correct dataword.
Example 10.3

## Slide 19
1. Comparing the received codeword with the first codeword in the table (01001 versus 00000), the receiver decides that the first codeword is not the one that was sent because there are two different bits.
2. By the same reasoning, the original codeword cannot be the third or fourth one in the table.
3. The original codeword must be the second one in the table because this is the only one that differs from the received codeword by 1 bit. The receiver replaces 01001 with 01011 and consults the table to find the dataword 01.
Example 10.3 (continued)

## Slide 20
Table 10.2 A code for error correction (Example 10.3)

## Slide 21
The Hamming distance between two words is the number of differences between corresponding bits.
Note

## Slide 22
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
Example 10.4
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 23
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Note

## Slide 24
Find the minimum Hamming distance of the coding scheme in Table 10.1.
Solution
We first find all Hamming distances.
Example 10.5
The dmin in this case is 2.

## Slide 25
Find the minimum Hamming distance of the coding scheme in Table 10.2.
Solution
We first find all the Hamming distances.
The dmin in this case is 3.
Example 10.6

## Slide 26
To guarantee the detection of up to s errors in all cases, the minimum
Hamming distance in a block code must be dmin = s + 1.
Note

## Slide 27
The minimum Hamming distance for our first code scheme (Table 10.1) is 2. This code guarantees detection of only a single error. For example, if the third codeword (101) is sent and one error occurs, the received codeword does not match any valid codeword. If two errors occur, however, the received codeword may match a valid codeword and the errors are not detected.
Example 10.7

## Slide 28
Our second block code scheme (Table 10.2) has dmin = 3. This code can detect up to two errors. Again, we see that when any of the valid codewords is sent, two errors create a codeword which is not in the table of valid codewords. The receiver cannot be fooled.
However, some combinations of three errors change a valid codeword to another valid codeword. The receiver accepts the received codeword and the errors are undetected.
Example 10.8

## Slide 29
Figure 10.8 Geometric concept for finding dmin in error detection

## Slide 30
Figure 10.9 Geometric concept for finding dmin in error correction

## Slide 31
To guarantee correction of up to t errors in all cases, the minimum Hamming distance in a block code must be dmin = 2t + 1.
Note

## Slide 32
A code scheme has a Hamming distance dmin = 4. What is the error detection and correction capability of this scheme?
Solution
This code guarantees the detection of up to three errors (s = 3), but it can correct up to one error. In other words, if this code is used for error correction, part of its capability is wasted. Error correction codes need to have an odd minimum distance (3, 5, 7, . . . ).
Example 10.9

## Slide 33
10-3 LINEAR BLOCK CODES
Almost all block codes used today belong to a subset called linear block codes. A linear block code is a code in which the exclusive OR (addition modulo-2) of two valid codewords creates another valid codeword.
Minimum Distance for Linear Block Codes Some Linear Block Codes
Topics discussed in this section:

## Slide 34
In a linear block code, the exclusive OR (XOR) of any two valid codewords creates another valid codeword.
Note

## Slide 35
Let us see if the two codes we defined in Table 10.1 and Table 10.2 belong to the class of linear block codes.
1. The scheme in Table 10.1 is a linear block code because the result of XORing any codeword with any other codeword is a valid codeword. For example, the XORing of the second and third codewords creates the fourth one.
2. The scheme in Table 10.2 is also a linear block code. We can create all four codewords by XORing two other codewords.
Example 10.10

## Slide 36
In our first code (Table 10.1), the numbers of 1s in the nonzero codewords are 2, 2, and 2. So the minimum Hamming distance is dmin = 2. In our second code (Table 10.2), the numbers of 1s in the nonzero codewords are 3, 3, and 4. So in this code we have dmin = 3.
Example 10.11

## Slide 37
A simple parity-check code is a single-bit error-detecting code in which n = k + 1 with dmin = 2.
Note

## Slide 38
Table 10.3 Simple parity-check code C(5, 4)

## Slide 39
Figure 10.10 Encoder and decoder for simple parity-check code
r0 = a3 + a2 + a1 + a0 modulo 2
s0 = b3 + b2 + b1 + b0 + q0 modulo 2

## Slide 40
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
1. No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
2. One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
3. One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.
Example 10.12

## Slide 41
4. An error changes r0 and a second error changes a3 .
The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that
here the dataword is wrongly created due to the
syndrome value.
5. Three bits—a3, a2, and a1—are changed by errors. The received codeword is 01011. The syndrome is 1. The dataword is not created. This shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.
Example 10.12 (continued)

## Slide 42
A simple parity-check code can detect an odd number of errors.
Note

## Slide 43
Figure Two-dimensional parity-check code

## Slide 44
Figure 10.11 Two-dimensional parity-check code

## Slide 45
Figure 10.11 Two-dimensional parity-check code

## Slide 46
All Hamming codes discussed in this book have dmin = 3.
Note

## Slide 47
Table 10.4 Hamming code C(7, 4)

## Slide 48
Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 49
Table 10.5 Logical decision made by the correction logic analyzer
r0 = a1 + a0 + a3 modulo 2
r1 = a3 + a2 + a1 modulo 2
r2 = a2 + a1 + a0 modulo 2
s0 = b1 + b0 + b3 + q0 modulo 2
s1 = b3 + b2 + b1 + q1 modulo 2
s2 = b2 + b1 + b0 + q2 modulo 2

## Slide 50
Let us trace the path of three datawords from the sender to the destination:
1. The dataword 0100 becomes the codeword 0100011. The codeword 0100011 is received. The syndrome is 000, the final dataword is 0100.
2. The dataword 0111 becomes the codeword 0111001. The syndrome is 011. After flipping b2 (changing the 1 to 0), the final dataword is 0111.
3. The dataword 1101 becomes the codeword 1101000. The syndrome is 101. After flipping b0, we get 0000, the wrong dataword. This shows that our code cannot correct two errors.
Example 10.13

## Slide 51
We need a dataword of at least 7 bits. Calculate values of k and n that satisfy this requirement.
Solution
We need to make k = n − m greater than or equal to 7, or 2m − 1 − m ≥ 7.
1. If we set m = 3, the result is n = 23 − 1 and k = 7 − 3, or 4, which is not acceptable.
2. If we set m = 4, then n = 24 − 1 = 15 and k = 15 − 4 = 11, which satisfies the condition. So the code is
Example 10.14
C(15, 11)

## Slide 52
Figure 10.13 Burst error correction using Hamming code

## Slide 53
10-4 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Cyclic Redundancy Check Hardware Implementation Polynomials Cyclic Code Analysis
Advantages of Cyclic Codes Other Cyclic Codes
Topics discussed in this section:

## Slide 54
Table 10.6 A CRC code with C(7, 4)

## Slide 55
Figure 10.14 CRC encoder and decoder

## Slide 56
Figure 10.15 Division in CRC encoder

## Slide 57
Figure 10.16 Division in the CRC decoder for two cases

## Slide 58
Figure 10.17 Hardwired design of the divisor in CRC

## Slide 59
Figure 10.18 Simulation of division in CRC encoder

## Slide 60
Figure 10.19 The CRC encoder design using shift registers

## Slide 61
Figure 10.20 General design of encoder and decoder of a CRC code

## Slide 62
Figure 10.21 A polynomial to represent a binary word

## Slide 63
Figure 10.22 CRC division using polynomials

## Slide 64
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.
Note

## Slide 65
In a cyclic code,
If s(x) ≠ 0, one or more bits is corrupted.
If s(x) = 0, either
a. No bit is corrupted. or
b. Some bits are corrupted, but the decoder failed to detect them.
Note

## Slide 66
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
Note

## Slide 67
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
Note

## Slide 68
Which of the following g(x) values guarantees that a single-bit error is caught? For each case, what is the error that cannot be caught?
a. x + 1 b. x3 c. 1
Solution
a. No xi can be divisible by x + 1. Any single-bit error can be caught.
b. If i is equal to or greater than 3, xi is divisible by g(x). All single-bit errors in positions 1 to 3 are caught.
c. All values of i make xi divisible by g(x). No single-bit error can be caught. This g(x) is useless.
Example 10.15

## Slide 69
Figure 10.23 Representation of two isolated single-bit errors using polynomials

## Slide 70
If a generator cannot divide xt + 1 (t between 0 and n – 1),
then all isolated double errors can be detected.
Note

## Slide 71
Find the status of the following generators related to two isolated, single-bit errors.
a. x + 1 b. x4 + 1 c. x7 + x6 + 1 d. x15 + x14 + 1
Solution
a. This is a very poor choice for a generator. Any two errors next to each other cannot be detected.
b. This generator cannot detect two errors that are four positions apart.
c. This is a good choice for this purpose.
d. This polynomial cannot divide xt + 1 if t is less than 32,768. A codeword with two isolated errors up to 32,768 bits apart can be detected by this generator.
Example 10.16

## Slide 72
A generator that contains a factor of x + 1 can detect all odd-numbered errors.
Note

## Slide 73
❏ All burst errors with L ≤ r will be detected.
❏ All burst errors with L = r + 1 will be detected with probability 1 – (1/2)r–1.
❏ All burst errors with L > r + 1 will be detected with probability 1 – (1/2)r.
Note

## Slide 74
Find the suitability of the following generators in relation to burst errors of different lengths.
a. x6 + 1 b. x18 + x7 + x + 1 c. x32 + x23 + x7 + 1
Solution
a. This generator can detect all burst errors with a length less than or equal to 6 bits; 3 out of 100 burst errors with length 7 will slip by; 16 out of 1000 burst errors of length 8 or more will slip by.
Example 10.17

## Slide 75
b. This generator can detect all burst errors with a length less than or equal to 18 bits; 8 out of 1 million burst errors with length 19 will slip by; 4 out of 1 million burst errors of length 20 or more will slip by.
c. This generator can detect all burst errors with a length less than or equal to 32 bits; 5 out of 10 billion burst errors with length 33 will slip by; 3 out of 10 billion burst errors of length 34 or more will slip by.
Example 10.17 (continued)

## Slide 76
A good polynomial generator needs to have the following characteristics:
1. It should have at least two terms.
2. The coefficient of the term x0 should be 1.
3. It should not divide xt + 1, for t between 2 and n-1.
4. It should have the factor x + 1.
Note

## Slide 77
Table 10.7 Standard polynomials

## Slide 78
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement Internet Checksum
Topics discussed in this section:

## Slide 79
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Example 10.18

## Slide 80
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.
Example 10.19

## Slide 81
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.
Example 10.20

## Slide 82
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9. Another way to find the complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).
Example 10.21

## Slide 83
Let us redo Exercise 10.19 using one’s complement arithmetic. Figure 10.24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color). The result is 36. However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6. In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6 = 9). The sender now sends six data items to the receiver including the checksum 9.
Example 10.22

## Slide 84
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.
Example 10.22 (continued)

## Slide 85
Figure 10.24 Example 10.22

## Slide 86
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Note

## Slide 87
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.
Note

## Slide 88
Let us calculate the checksum for a text of 8 characters (“Forouzan”). The text needs to be divided into 2-byte (16-bit) words. We use ASCII (see Appendix A) to change each byte to a 2-digit hexadecimal number. For example, F is represented as 0x46 and o is represented as 0x6F. Figure 10.25 shows how the checksum is calculated at the sender and receiver sites. In part a of the figure, the value of partial sum for the first column is 0x36. We keep the rightmost digit (6) and insert the leftmost digit (3) as the carry in the second column. The process is repeated for each column. Note that if there is any corruption, the checksum recalculated by the receiver is not all 0s. We leave this an exercise.
Example 10.23

## Slide 89
Figure 10.25 Example 10.23